## Slide 1
Proposal for Grant Giovani CSN5 - Year 2026
- Acronym: PROGETTO (placeholder, final acronym to be defined)
- Full title: Laboratory fluorescence-XAS for realistic and operando-compatible energy-material samples
- Applicant: Simone Manti
- Main unit: INFN Laboratori Nazionali di Frascati
- External scientific case: battery materials, potentially with ENEA collaboration
- Strategic extension: transferability to EuAPS and compact pulsed X-ray sources
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 2
Summary
- The project develops a laboratory fluorescence-XAS platform for realistic samples where transmission XAS is impractical or unrepresentative.
- The benchmark case is redox-active battery materials, with emphasis on Fe/Mn/Ni K-edge observables relevant to oxidation state and local coordination.
- The central challenge is the coupled trade-off between source acceptance, energy resolution, fluorescence efficiency, background, SDD rate capability, and scan time.
- The expected result is a validated operating domain for laboratory fluorescence-XAS, from reference compounds to battery samples in controlled electrochemical states.
- EuAPS is treated as a strategic compact-source application: requirements and feasibility will be derived from the validated laboratory platform.
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 3
1 State of the Art
- Synchrotron XAS provides high-quality operando data but is access-limited and poorly suited to rapid laboratory screening cycles.
- Laboratory transmission XAS is established but usually requires thin, homogeneous, and carefully prepared samples.
- Fluorescence XAS is better matched to realistic, thick, dilute, or cell-integrated samples, but laboratory implementations are constrained by low useful flux and background.
- Commercial laboratory XAS systems exist, but they are often black-box instruments and are not optimized for INFN-specific modularity, detector studies, or compact-source transferability.
- VOXES demonstrated INFN expertise in crystal-based X-ray spectroscopy with efficient use of laboratory sources.
- The open gap is a quantitatively validated, modular fluorescence-XAS methodology for realistic energy-material samples.
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 4
1 State of the Art - Capability Gap
- The innovation is not generic laboratory XAS.
- The missing capability is fluorescence-XAS on realistic samples with measured limits on chemical sensitivity, acquisition time, and reproducibility.
- The key performance question is: how much source phase space can be accepted while preserving useful XANES/EXAFS information?
- A successful platform must co-optimize crystal optics, slits, sample geometry, SDD solid angle, background suppression, and data analysis.
- The project will turn this trade-off into quantitative design rules and validated measurements.
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 5
2 Objectives and Expected Results
- O1: Define target samples, absorption edges, and measurable XAS observables for battery-relevant materials.
- ER1: Performance requirements for edge-shift sensitivity, SNR, energy resolution, and scan time.
- O2: Design and integrate a modular laboratory fluorescence-XAS geometry.
- ER2: Calibrated platform with controlled source, optics, sample, detector, and DAQ chain.
- O3: Validate the platform on reference compounds and realistic static or ex-situ battery samples.
- ER3: Demonstrated extraction of oxidation-state and local-structure indicators.
- O4: Assess operando compatibility and EuAPS transferability.
- ER4: Feasibility report, design requirements, and optional pilot test if conditions allow.
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 6
3 Methodology - Overall Strategy
- Start from a specific scientific use case rather than from hardware procurement.
- Use simulations to define the required flux, energy resolution, detector rate, and background rejection.
- Build or adapt only the components required by the performance budget.
- Validate progressively: reference compounds, realistic ex-situ samples, controlled electrochemical states, operando-compatible measurements.
- Treat EuAPS as a transferability study based on measured requirements, not as the main success criterion.
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 7
3 Methodology - Work Packages
- WP1 - Simulation and performance budget: source, crystal optics, slits, sample, fluorescence yield, detector rate, background, and SNR.
- WP2 - Platform integration: crystal optics, stages, collimation, shielding, sample-detector geometry, SDD/DAQ, and calibration routines.
- WP3 - Reference and static validation: Fe/Mn/Ni/Cu compounds and selected battery samples in known chemical states.
- WP4 - Operando-compatible demonstration: slow electrochemical cycling if feasible; ex-situ state series as fallback.
- WP5 - Compact-source transferability: EuAPS source model, layout requirements, timing/rate constraints, and optional pilot measurement.
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 8
3 Methodology - Measurable Performance
- Energy calibration and resolution measured on reference foils or compounds.
- Sensitivity to edge shifts of order 1 eV, depending on selected edge and sample system.
- White-line and near-edge intensity variations quantified with repeatability tests.
- SNR and acquisition time measured for each sample class.
- Detector dead-time and pile-up characterized for fluorescence count rates.
- Simulation-to-data agreement used as a design validation metric.
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 9
4 Organization
- Applicant: responsible for spectroscopy design, simulations, integration, measurements, analysis, and project coordination.
- INFN LNF: host structure, X-ray spectroscopy expertise, mechanical/electronics support, safety framework, and existing VOXES know-how.
- ENEA or equivalent battery-material partner: sample selection, electrochemical preparation, cell know-how, and interpretation of battery-relevant results.
- Possible advisors: crystal spectroscopy, detector/DAQ, electrochemistry, and compact-source instrumentation.
- The team should remain small and credible, with clear FTEs and no dependence on undefined external labor.
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 10
4 Organization - Milestones and Deliverables
Year 1
Year 2
- M1: sample and edge selection frozen
- M2: performance budget completed
- M3: detector and geometry requirements frozen
- D1: simulation/design report
- D2: integrated fluorescence-XAS platform
- D3: calibration and reference-measurement report
- M4: realistic battery-sample validation completed
- M5: operando-compatible geometry assessed
- M6: EuAPS transferability requirements defined
- D4: battery-material XAS demonstration report
- D5: compact-source feasibility report
- D6: manuscript or technical note
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 11
5 Synergies with External Projects
- ENEA collaboration: battery materials, electrochemical states, possible cells, and interpretation of redox behavior.
- VOXES/LNF know-how: HAPG crystals, crystal-spectrometer alignment, laboratory X-ray measurements, and analysis procedures.
- EuAPS: possible future deployment of the validated methodology to compact pulsed X-ray sources.
- DAFNE-Light or other LNF activities: possible benchmark and broader use of laboratory X-ray diagnostics.
- Detector and electronics groups: SDD evaluation, DAQ integration, pile-up/dead-time studies, and synchronization.
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 12
6 Impact and Spin-offs
- Scientific impact: routine pre-screening and mechanistic studies of redox-active materials before synchrotron campaigns.
- INFN impact: reusable platform for fluorescence-XAS, detector/readout characterization, and compact-source diagnostics.
- Interdisciplinary impact: stronger bridge between X-ray instrumentation and energy-material research.
- Technology-transfer potential: modular laboratory diagnostics for battery, catalysis, and materials laboratories.
- Long-term spin-off: design rules for XAS at compact laser-plasma sources, including EuAPS.
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 13
7 Costs
- Budget principle: every requested item must support the primary laboratory fluorescence-XAS goal.
- Year 1 likely items: SDD or detector module if required, motorized stages, collimators/slits, shielding, crystals or optics, mechanics, DAQ/control hardware.
- Year 2 likely items: operando-cell adapters, sample holders, consumables, reference compounds, missions to ENEA or benchmark facilities, publication/conference costs.
- No hardware should be justified only by EuAPS unless it is also needed by the primary platform.
- No funds for research contracts or third-party appointments, in line with the call.
- All equipment requests above 2 kEuro must be supported by detailed quotations.
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 14
7 Costs - Draft Budget Logic
- Detector: existing SDD first; purchase only if active area, rate, energy resolution, or DAQ constraints require it.
- Motion and mechanics: modular stages for energy scan, sample positioning, and detector geometry.
- Optics and shielding: components selected from the performance budget, not from a generic setup wish list.
- Electrochemical/sample environment: minimal cell and holder development for controlled sample states.
- EuAPS: limited to compatibility design and possible mission/pilot test, unless shared hardware is justified.
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 15
8 Risk Assessment
- Risk: fluorescence rate too low for operando measurements. Mitigation: static/ex-situ state series and longer integration on selected states.
- Risk: background prevents useful XANES sensitivity. Mitigation: shielding, geometry optimization, SDD energy windows, and reference subtraction.
- Risk: SDD rate capability or pile-up is inadequate. Mitigation: detector comparison, shaping-time optimization, collimation, and dead-time correction.
- Risk: operando cell is not ready within the project timeline. Mitigation: controlled electrochemical states prepared with ENEA.
- Risk: EuAPS is not available or not stable. Mitigation: EuAPS deliverable limited to transferability requirements and layout study.
- Risk: novelty is perceived as generic lab XAS. Mitigation: emphasize quantified operating domain on realistic samples and measured chemical sensitivity.
Grant Giovani CSN5 2026 - PROGETTO draft

## Slide 16
9 Bibliography
- P. Zimmermann et al., Modern X-ray spectroscopy: XAS and XES in the laboratory, Coord. Chem. Rev. 423, 213466 (2020).
- S. Manti et al., Enhancing Performances of the VOXES Bragg Spectrometer for XES Investigations, Condens. Matter 9, 19 (2024).
- S. Manti and A. Scordo, Recent Developments of the VOXES Von Hamos X-Ray Spectrometer for Laboratory XES and XAS Studies, Eng. Innov. 19, 23-29 (2026).
- F. Galdenzi et al., The EuAPS Betatron Radiation Source: Status Update and Photon Science Perspectives, Condens. Matter 9, 30 (2024).
- Add selected battery-material XAS and operando-XAS references after choosing the ENEA sample system.
- Add commercial/laboratory fluorescence-XAS references to define the exact state-of-the-art boundary.
Grant Giovani CSN5 2026 - PROGETTO draft